## Slide 1: HP 27S SCREEN REPLACEMENT
ANDREW CHILDS

## Slide 2: About the 27S
Algebraic Scientific Calculator
Saturn Architecture
Manufacture 1988 – 1991
Programmable through Solver
Ebay purchase £50
Early life LCD failure- very clean unit

## Slide 3: Case Removal
Prize the case apart with back of tweezers – ‘defeating 7Nr heat stakes’.
Donor screen – From HP17B

## Slide 4: 17B vs 27S
Main PCB part number
17B:- 5180-1532 BD Rev B-2645
27S:- 5180-1532 BD Rev B-2645
8k x8Bit Static CMOS RAM
17B also has a 32k x 8Bit MOS ROM

## Slide 5: Matching LCD
Model :
EPSON LD-B8807A-1

## Slide 6: More heat stakes!
Gently pull the head ‘flange’ up and cut off some material.
Lift the metal chassis with LCD

## Slide 7: LCD & Zebra Strips
Rubber zebra strips sit upon the LCD contacts and compress onto the gold-plated PCB contacts.
‘Cleanliness is next to godliness’!

## Slide 8: Rear of Keypad (and another common problem)

## Slide 9: Swap the chassis assy. Inc. Screen
Push through the heat stakes
Compress the chassis to keyboard
Melt the heat stakes

## Slide 10: Case Heat-Stakes
Heat with hot air
Form to cylindrical shape with tweezers – remove ‘mushroom’ shape head

## Slide 11: Finished HP 27S
No RPN calculators were harmed in this repair.
HP 17B and H27S share a platform in terms of (base) PCB, LCD, Chassis